## Slide 1
Presented By Mark Thoren
Flip Flop Fun!

## Slide 2: What is a Flip Flop?
The fundamental element of sequential logic
“When a rising clock edge comes along, copy whatever is at the DATA input to the Q output”
Questions:
How soon before the clock edge must the data be present? (or “set up”)
How long after the clock edge must the data be “held”
After the clock edge, how long does it take for the data to “propagate” from D to Q?
Copy

## Slide 3: Timing Details

## Slide 4: Preview: Thoren’s Favorite Interview Question
Question:
Does Q go Low or High?
Tie Data and Clock together, and drive with a square wave

## Slide 5: Why Care? FPGAS, and lots of other parts, are filled with flip flops
Anything that stores a digital state has a flip-flop or latch somewhere
SRAM: A bunch of individually addressable flip-flops
Microprocessor – flip flops wrapped with logic and control
MC14500 1-bit “Industrial Control Unit” Block Diagram
1-bit result flip-flop (register)
Gaming on a 1-bit computer? You bet!

## Slide 6: You can also buy them as “discrete” components
74x74 - Dual D-type Flip-Flop with Set and Reset
74x109 – Dual J-K FF with Reset
74x273 – Octal D FF (with global reset
74x273

## Slide 7: Typical SPI Controller / Target Relationship
D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
Controller (MAX32690 Microcontroller)
Target (AD7124-8 ADC)
D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
Serial Peripheral Interface (SPI)
Data to Transmit
Data Recieved
Data to Transmit
Data Recieved
MISO
MOSI
SCK
…
…
CS
CS
CS
CS
CS
SCK

## Slide 8: AD7124-8 SPI Interface Timing Specs

## Slide 9: MAX32690 µC SPI Interface Timing Specs

## Slide 10: FPGAs have more “knobs” (Timing Constraints)
Tell the FPGA tool the peripheral’s timing requirements, and it will try to meet them (and let you know if it can’t)
But this is a rabbit hole for another day…

## Slide 11: 74HC74 Refresher

## Slide 12: Timing
5 leading manufacturers…
 | NXP min typ max |  |  | ST min typ max |  |  | ON min typ max |  |  | Fairchild min typ max |  |  | Toshiba min typ max |  | 
tsetup@2.0V | 75 | 6 |  | 75 | 15 |  | 80 |  |  | 80 | 35 |  | 75 |  | 
tsetup@4.5V | 15 | 2 |  | 15 | 4 |  | 16 |  |  | 16 | 10 |  | 15 |  | 
tsetup@6.0V | 13 | 2 |  | 13 | 3 |  | 14 |  |  | 14 | 8 |  | 13 |  | 
thold@2.0V | 3 | -6 |  | 0 |  |  | 3 |  |  | 0 |  |  | 0 |  | 
thold@4.5V | 3 | -2 |  | 0 |  |  | 3 |  |  | 0 |  |  | 0 |  | 
thold@6.0V | 3 | -2 |  | 0 |  |  | 3 |  |  | 0 |  |  | 0 |  | 
tprop@2.0V |  | 47 | 220 |  | 48 | 150 |  |  | 100 |  | 34 | 110 |  | 51 | 150
tprop@4.5V |  | 17 | 44 |  | 16 | 30 |  |  | 20 |  | 12 | 22 |  | 17 | 30
tprop@6.0V |  | 14 | 37 |  | 13 | 26 |  |  | 17 |  | 10 | 19 |  | 15 | 26
Zero Hold implies: data and clock can change simultaneously

## Slide 13: What happens when you just barely violate timing?
Source:
W. J. Dally, Lecture notes for EE108A, Lecture 13: Metastability and Synchronization Failure (When Good Flip-Flops go Bad) 11/9/2005.
“Metastability”! Another rabbit hole we’re about to dive into.
Source:
01signal: Metastability and the basics of clock domain crossing. (n.d.). https://www.01signal.com/verilog-design/clockdomains/crossing-basics/
(Also essential reading from 01signal: “Electronic Exorcism: Why FPGAs sometimes behave as if they are possessed”)

## Slide 14: Let’s Design Some Circuits…
Then build…
Then test…

## Slide 15: Input Thresholds
5 leading manufacturers…
 | NXP min typ max |  |  | ST min typ max |  |  | ON min typ max |  |  | Fairchild min typ max |  |  | Toshiba min typ max |  | 

## Slide 16: Probing…
Sometimes probing is “inaccessible technology”
  Agilent N2750 1.5 GHz diff probe: $4800
  U1818A 7 GHz diff probe: $9500
  Nexus Technology interposers and probes… don’t ask.

## Slide 17: Microcontroller/processor peripherals
EVERY input and output has a flip flop (or “register”) at some point
UART, I2C, and SPI are “shift registers”, or strings of flip flops
  UART – Shift register clocked at a fixed rate
  SPI – Controller and target shift registers share a common clock
  I2C – Defined timing requirements

## Slide 18
Thank You! <and/or> Questions? <and/or> Section Slide